## Slide 1
Brief Introduction of
Y27Plex STR Detection Kit
Jiangsu Superbio Biomedical (Nanjing) Co.,Ltd.
May 2023

## Slide 2
Features of Y27Plex

## Slide 3
1.1 Features of Y27Plex STR Detection Kit
1. Y27Plex is a 5-color fluorescence detection product which is applicable for performing multiple amplification and detection on 27 Y-STR loci.
2. Y27Plex features better compatibility and higher accuracy. The detected loci include 20 low-mutating STRs (mutating rate<1%) and 7 rapid-mutating loci (mutating rate>1%).
3. Y27Plex is suitable for male family investigation, featuring high discrimination power (DP).
4. Y27Plex is suited best for Y-STR library building, as it contains all mainstream loci that are required.
5. Strong compatibility. Y27Plex is compatible with the direct amplification of various samples and the amplification of purified DNA.
6. Rapid amplification.The whole PCR process using Y27Plex takes less than 120min.
7. Applicable for forensic analysis, kinship detection and scientific research for human genetic identification.

## Slide 4
1.2 Loci Arrangement Diagram of Y27Plex

## Slide 5
1.3 Analysis Software Loci Information Table of Y27Plex
GeneMapper ID-X version 1.3

## Slide 6
1.4 Electrophoretic Diagram of Y27Plex Allelic Ladder
Y27Plex Allelic Ladder contains 266 alleles

## Slide 7
General Information of Y27Plex

## Slide 8
2.1 Y27Plex STR Detection Kit (25µL× 100 RXN/Kit)
 | Component | Content | Description
Pre-amplification Kit | 2.5× PCR Mix | 1,000μL× 1 | Buffer containing anti-inhibition components such as MgCl2
 | Y27Plex Primers | 500μL× 1 | Primer mixtures for amplifying 27 loci
 | PCR Grade Water | 1,000μL× 1 | Nuclease-free deionized ultrapure water
 | Control DNA 9948 (0.5ng/µL) | 20μL× 1 | Standard positive control
 | Control DNA 9947A (0.5ng/µL) | 20μL× 1 | Standard negative control
 | Taq DNA Polymerase | 100μL× 1 | Hot-start DNA Polymerase
Post-amplification Kit | Y27Plex Allelic Ladder | 20μL× 1 | Contains amplified alleles
 | Orange-500 | 75μL× 1 | Internal lane standards with fluorescent markers
Matrix Kit | 5 Dye Matrix | 50μL×1 | Used for spectral calibration

## Slide 9
2.2 Reaction System and Procedures of Y27Plex STR Detection Kit
Component | 25µL System (µL)
2.5× PCR Mix | 10.0
Y27Plex Primers | 5.0
PCR Grade Water | 8.0
Control DNA 9948 (0.5ng/µL) | 1.0
Taq DNA Polymerase | 1.0
Total Volume | 25.0
95℃
2min
94℃
20sec
59℃
1min
72℃
1min
60℃
30min
16℃
∞
30 Cycles

## Slide 10
Amplification Results of Y27Plex

## Slide 11
3.1 Amplification Results of Positive Control 9948 Analyzed on 3130xl

## Slide 12
3.2 Amplification Results of Blood on FTA Analyzed on 3130xl

## Slide 13
3.3 Amplification Results of Blood on Filter Paper Analyzed on 3130xl

## Slide 14
3.4 Amplification Results of Saliva on FTA Analyzed on 3130xl

## Slide 15
Performance Measurement of Y27Plex

## Slide 16
4.1 Sensitivity Test
4.1.1 Content of Extracted DNA
• 1ng, 500pg, 250pg, 125pg, 62.5pg, 31.25pg
• Repeat the experiment 3 times for all samples
4.1.2 Number of Direct Amplification Samples
FTA Blood Card
• 1, 2 or 3 slices - 1.2mm aperture
• Repeat the experiment 3 times for all samples
FTA Saliva Card
• 1, 2 or 3 slices - 1.2mm aperture
• Repeat the experiment 3 times for all samples

## Slide 17
4.1.1 Extracted DNA
30 cycles
25μL amplification system
3130xl (3kV, 10sec sampling time)
Baseline threshold 50RFU

## Slide 18
4.1.1 Extracted DNA
500pg
250pg
125pg
62.5pg
1ng
31.25pg

## Slide 19
4.1.2 Number of Direct Amplified Samples -- FTA Blood Card & FTA Saliva Card
30 cycles
25μL amplification system
3130xl (3kV, 10sec sampling time)
Baseline threshold 50RFU

## Slide 20
4.1.2 Number of Direct Amplified Samples -- FTA Blood Card & FTA Saliva Card
1 – 1.2mm punch, Blood
1 – 1.2mm punch, Buccal
2 – 1.2mm punches, Blood
2 – 1.2mm punches, Buccal
3 – 1.2mm punches, Blood
3 – 1.2mm punches, Buccal

## Slide 21
4.2 Tolerance Test
4.2.1 Mix Concentration
• 0.75 x, 1 x, 1.25 x
4.2.2 Primer Concentration
• 0.75 x, 1 x, 1.25 x
4.2.3 Annealing Temperature
• 55℃, 57 ℃, 59 ℃, 61 ℃
4.2.4 Cycles Number
• 28, 29, 30, 31
4.2.5 Reaction Volume
• 25µl and 10µl

## Slide 22
4.2.1 Concentrations of Mix and Primer
30 cycles
25μL amplification system
3130xl (3kV, 10sec sampling time)
Baseline threshold 50RFU

## Slide 23
4.2.1 Mix Concentration
0.75 X, Blood
0.75 X, Buccal
1.00 X, Blood
1.00 X, Buccal
1.25 X, Blood
1.25 X, Buccal

## Slide 24
4.2.2 Primer Concentration
0.75 X, Blood
0.75 X, Buccal
1.00 X, Blood
1.00 X, Buccal
1.25 X, Blood
1.25 X, Buccal

## Slide 25
4.2.3 Annealing Temperature
30 cycles
25μL amplification system
3130xl (3kV, 10sec sampling time)
Baseline threshold 50RFU

## Slide 26
4.2.3 Annealing Temperature — FTA Blood Card
55℃, Blood
57 ℃, Blood
59℃, Blood
61 ℃, Blood

## Slide 27
4.2.3 Annealing Temperature — FTA Saliva Card
55℃, Buccal
57 ℃, Buccal
59℃, Buccal
61 ℃, Buccal

## Slide 28
4.2.4 Cycles Number — 28-31 (25 μL)
25μL Reaction Volume

## Slide 29
4.2.4 Cycles Number — 28-31 (10 μL)
10μL Reaction Volume

## Slide 30
4.2.5 Reaction Volume
25μL, extracted DNA
10μL, extracted DNA
25μL, Blood
10μL, Blood
25μL, Buccal
10μL, Buccal

## Slide 31
4.3 Inhibition Test
Three kinds of inhibitors:
4.3.1 Hematin
• 0.1, 0.2, 0.3 and 0.4mM
4.3.2 Hemoglobin
• 80, 100, 200 and 300µM
4.3.3 Humic Acid
• 10, 30, 50 and 100ng/µL

## Slide 32
4.3 Inhibition Test
30 cycles
25μL amplification system
3130xl (3kV, 10sec sampling time)
Baseline threshold 50RFU

## Slide 33
4.3.1 Hematin
0.1 mM
0.2 mM
0.3 mM
0.4 mM

## Slide 34
4.3.2 Hemoglobin
60 μM
100 μM
200 μM
300 μM

## Slide 35
4.3.3 Humic Acid
10 ng/μL
30 ng/μL
50 ng/μL
100 ng/μL

## Slide 36
4.4 Summary
1. High sensitivity: Y27Plex showed good performance in the amplification of 0.25ng DNA samples. 1-3 pieces of FTA blood cards and/or FTA oral cards of 1.2 mm aperture were amplified normally.
2. Strong tolerance: Y27Plex amplified normally in Mix or Primer reaction systems of different concentrations. Y27Plex showed good performance at 55 - 61°C annealing temperature or 29 - 31 reaction cycles.
3. Strong resistance to multiple inhibitors: Y27Plex amplified normally under conditions of 0.2mM hematin, 200μM hemoglobin or 30ng/μL humic acid.

## Slide 37
4.4 Summary
 | AB Yfiler | AB Yfilerplus | Goldeneye 27Y | Yesu 27Y | Data Y30 | PP Y23
DYS19 |  |  |  |  |  | 
DYS389I |  |  |  |  |  | 
DYS389II |  |  |  |  |  | 
DYS390 |  |  |  |  |  | 
DYS391 |  |  |  |  |  | 
DYS392 |  |  |  |  |  | 
DYS393 |  |  |  |  |  | 
DYS385 a |  |  |  |  |  | 
DYS385 b |  |  |  |  |  | 
DYS438 |  |  |  |  |  | 
DYS439 |  |  |  |  |  | 
DYS437 |  |  |  |  |  | 
DYS448 |  |  |  |  |  | 
DYS456 |  |  |  |  |  | 
DYS458 |  |  |  |  |  | 
DYS635 |  |  |  |  |  | 
GATA-H4 |  |  |  |  |  | 
DYS533 |  |  |  |  |  | 
DYS481 |  |  |  |  |  | 
DYS460 |  |  |  |  |  | 
DYS518 |  |  |  |  |  | 
DYS570 |  |  |  |  |  | 
DYF387S1a |  |  |  |  |  | 
DYF387S1b |  |  |  |  |  | 
DYS449 |  |  |  |  |  | 
DYS576 |  |  |  |  |  | 
DYS627 |  |  |  |  |  | 
DYS527ab |  |  |  |  |  | 
DYS549 |  |  |  |  |  | 
DYS643 |  |  |  |  |  | 
DYS522 |  |  |  |  |  | 
DYS444 |  |  |  |  |  | 
DYS520 |  |  |  |  |  | 
DYS557 |  |  |  |  |  | 
DYS388 |  |  |  |  |  | 
DYS447 |  |  |  |  |  | 

## Slide 38
5
10
15
20
25
Mb
DYS393
DYS456
DYS458
DYS19
DYS390
GATA-H4
DYS385a
DYS385b
DYS392
DYS448
DYS391
DYS635
DYS437
DYS439
DYS438
DYS389Ⅰ/Ⅱ
30
p
q
AMEL Y
9 small haplotype loci
2 SWGDAM recommended loci
4.4 Summary

## Slide 39
Service & Cooperation

## Slide 40
Service & Cooperation
Jiangsu Superbio Biomedical Co. Ltd., founded in 2011, is a cutting-edge technology enterprise owning the Practice License of Medical Institution, which specializes in the research and testing of gene sequencing industry, and integrates R&D, production and sales. The company's products and services cover forensic testing, medical testing, food/environment/medicine testing, instrumentation and software.
We are willing to provide clients with scientific research services related to forensic DNA testing, such as research projects and papers publication, solving all the difficulties encountered in the experiment for you.
We sincerely look forward to cooperate with you in developing products and researching projects.

## Slide 41
THANKS!
Contact Us
Address: Sino-Danish Ecological Life Science Industrial Park, No.3-1 Xinjinxhu Road, Pukou District, Nanjing
Tel: 400-616-2676
Website: http://www.superbio.cn/